## Slide 1: CHAPTER 13: Ethernet and TCP-IP Networking
The Architecture of Computer Hardware, Systems Software & Networking: An Information Technology Approach
4th Edition, Irv Englander
John Wiley and Sons 2010

## Slide 2: Chapter Example
User sitting at a computer types a URL that contains a domain name into a web browser
First, HTTP client obtains the IP address of the Web server
Then HTTP client initiates the process with a request to the TCP socket to establish a logical connection with the HTTP server at the destination site

## Slide 3: Domain Names and DNS Services
Domain Names
  Hierarchical system of network address identifiers used throughout the Internet and on local area networks, intranets and extranets
  Created so users would not have to memorize IP addresses
Domain Name System (DNS)
  Domain name resolution – translates domain names into IP addresses
  Uses a massive distributed database containing a directory system of servers
  Each entry contains a domain name and an associated IP address

## Slide 4: Domain Name System (DNS)
DNS Server Hierarchy
The Elements of a Domain Name

## Slide 5: Top Domain Name Registrations

## Slide 6: Domain Name Resolution

## Slide 7: Transport Layer
TCP protocol
  Sends a packet to TCP at the destination site, requesting a connection
  Handshaking – back and forth series of requests and acknowledgments
  If handshaking negotiations are successful, a connection is opened
  Connection is logically full-duplex

## Slide 8: Three-Way TCP Connection Handshake

## Slide 9: TCP Segment Format

## Slide 10: Network Layer
IP protocol
  Responsible for relaying packets from the source end node to the destination end node through intermediate nodes
  Performed using datagram packet switching and logical IP addresses
  Best-attempt unreliable service
  Size of datagram ranges from 20 to 65,536 bytes
  Header size between 20 and 60 bytes

## Slide 11: IPv4 Addresses
Registered and allocated by ICANN
32 bits long divided into 4 octets
Assigned in blocks of contiguous addresses
  Number of addresses is a power of two
Divided into three levels
  Network address
  Subnetworks (subnets)
  Hosts (nodes)
Masks
  Used to separate the different parts of the address

## Slide 12: IPv4 Datagram Format

## Slide 13: IP Addresses
IP Block Addresses
IP Hierarchy and Subnet Mask

## Slide 14: Reseved IP Addresses

## Slide 15: DHCP
  Two methods to distribute IP addresses more efficiently:
  Use of private network IP addresses behind a router
    The router must readdress traffic passing between the Internet and the local network
    Management of readdressing becomes difficult with large networks
Dynamic Host Configuration Protocol (DHCP)
  Maintain a bank of available IP addresses and assign them dynamically to computers for use when the computers are attached to the network
  Method often used by large organizations, DSL and cable providers
  DHCP client on computer or network device broadcasts a query to locate the DHCP server
  DHCP server responds with a lease which includes an IP address, domain name of network, IP address of DNS server, subnet mask, IP address of gateway and other configuration parameters

## Slide 16: Operation of IP
Two major functions
  Routes datagrams from node to node until they reach their destination node
  Translates IP addresses to physical addresses before it passes the packets to the data link later for delivery
Address Resolution Protocol (ARP)
  Implemented at the network layer
  Translation of IP address to physical address at each intermediate node until destination is reached
  A broadcast of the IP address is sent to every node on the network. The matching node responds with a physical address
  Physical address (MAC address in the case of Ethernet) is sent in frame to the data link layer
  At final destination, the packet is passed up to the transport layer for deployment to the application layer

## Slide 17: Data Link Layer
Layer responsible for transmitting a packet from one node to the next node
Node access defined by the medium access control (MAC) protocol
  Steer data to its destination
  Detect errors
  Prevent collisions
Ethernet (CSMA-CD)
  Predominant medium-access protocol for local area networks
  Standard Ethernet packet is a frame (see next slide)

## Slide 18: Ethernet Frame

## Slide 19: Hub-Based Ethernet
Simple means of wiring a bussed Ethernet together
Logically still a bus network
CSMA-CD
Collision
  Occurs when multiple nodes access the network in such a way that their messages become mixed and garbled
Network propagation delay
  Amount of time that it takes for one packet to get from one end of the network to the other
Adequate for networks with light traffic

## Slide 20: Switched Ethernet
Permits point-to-point connection of any pair of nodes
Multiple pairs can be connected simultaneously
Possible to connect nodes in full-duplex mode
Each pair of connections operates at the maximum bit rate of the network
Why can’t there be any collisions in a switched Ethernet network?

## Slide 21: Quality of Service (QoS)
Methods to reserve and prioritize channel capacity to favor packets that require special treatment
Service guarantees from contract carrier services that specify particular levels of throughput, delay and jitter
  Jitter – variation in delay from packet to packet
Differentiated service (DiffServ)
  8-bit (DS) field in IP header
  Set by the application at the sender or by the first node
  Diffserv capable nodes such as routers can then prioritize and route packets based on the packet class

## Slide 22: Network Security Categories
Intrusion
  Keeping network and system resources free from intruders
Confidentiality
  Keeping the content of data private
Authentication
  Verifying the identity of a source of data being received
Data integrity and non-repudiation
  Protecting the content of data communication against changes and verifying the source of the message
Assuring network availability and access control
  Keep network resources operational and restricting access to those permitted to use them

## Slide 23: Network Security
Network intrusions
  Packet sniffers read data in a packet as it passes through a network
  Probing attacks to uncover IP address / port numbers that accept data packets
Physical and Logical Restriction
  Limit access to wiring and network equipment
  Firewall
  Private networks
Encryption
  Symmetric key cryptography
    Both key used for encryption and decryption
    Both sender and receiver use the same key which makes security difficult
  Public key cryptography
    Two different keys are used for encryption and decryption

## Slide 24: Alternative Protocols to TCP/IP
MPLS (Multi-Protocol Label Switching)
  Creates a virtual circuit over packet switched networks to improve forwarding speed of datagrams
ATM (Asynchronous Transfer Mode)
  Partial-mesh network technology in which data passes through the network in cells (53-byte packets)
SONET (Synchronous Optical Network) and
SDH (Synchronous Digital Hierarchy)
  Protocol that uses fiber optic to create wide area networks with very high bit rates over long distances
Frame Relay
  Slow, wide area network standard