## Slide 1: Network Fundamentals
Computer Information Systems
University of Louisville
Ghiyoung Im, PhD
CIS 480 – Intro to Network Security

## Slide 2: Objectives
Identify the basic network architectures.
Define the basic network protocols.
Explain routing and address translation.
Classify security zones.
understand principles behind network layer services
Learn about transport layer protocols in the Internet

## Slide 3: Network Fundamentals Outline
1. Basic Network Concepts
  Network Topologies
  Network Hardware
  Network Design
2. The OSI 7 Layers
3. Internet Protocol
  IPv4
  ARP & RARP
  IPv6
  DNS
4. Transport Protocol
  UDP
  TCP
  ICMP/IGMP
5. Packet Analysis
  IP
  TCP

## Slide 4: Network Architectures
Local area network (LAN)
  Typically smaller in terms of size and geographic coverage, and consists of two or more connected devices. Home networks and most small office networks can be classified as LANs.
MAN (Metropolitan Area Network)
Wide area network (WAN)
  Tends to be larger, covering more geographic area, and consists of two or more systems in geographically separated areas connected by any of a variety of methods.
Internet
  The global network that connects millions of systems.
Personal Area Networks (PAN)
  Wireless telecommunications network for device-to-device connections within a small range (e.g., Bluetooth)

## Slide 5: A-1: A Simple Home Network
* Panko, 2010

## Slide 6: A-4: Wide Area Networks (WANs)
* Panko, 2010

## Slide 7: A-5: The Internet
Network
Browser
Packet
Router
Packet
Router
Packet
Route
Webserver
Software
Router

## Slide 8: Network Topology
One major component of every network’s architecture is the network’s topology — how the network is physically or logically arranged
The main classes of network topologies are star, ring, bus, and mixed

## Slide 9: Physical Network Topologies
Star:
  Systems are connected to a central device
Bus:
  Systems are connected to the same cable segment
Ring
  Systems are connected to each other in a closed loop
Mixed:
  Larger networks may employ multiple topologies at the same time

## Slide 10: Network Topologies
* Wikipedia, 2011

## Slide 11: Categories of Network Topologies
Physical Topologies | Logical Topologies
The shape of the cabling layout used to link devices | The way that the data passes through the network from one device to the next without regard to the physical interconnection of the devices
Ring, Star, Tree | Ethernet, Token Ring
Determined by the physical layout of cables, wires, and network devices | Determined by network protocols
A network's logical topology is not necessarily the same as its physical topology. | - Ethernet: Logical bus topology in a physical star topology - Token Ring: Logical ring topology in a physical star topology
* Wikipedia, 2011

## Slide 12: Ethernet
The most popular media access protocol (layer 2) used on LANs
Local area network (LAN) technology developed by Xerox, Digital, Intel and commercialized in 1980 (IEEE 802.3)
Speed: 10 Mbps -> 10 Gbps
Shared media (bus topology)
  Development to Switched media (star topology): data is less public

## Slide 13: A-3: Building LAN
* Panko, 2010

## Slide 14: Ethernet MAC
Multiple user share the same media
Media Access Control: CSMA/CD (Carrier Sense Multiple Access w/ Collision Detection)
Steps for communication:
  Check whether a user is transmitting data
  Wait when the data is transmitted
  Monitor to check whether collusions occurred

## Slide 15: Ethernet: Unreliable, connectionless
Connectionless: No handshaking between sending and receiving NICs
Unreliable: receiving NIC doesn’t send ACKs or NACKs to sending NIC
  stream of datagrams passed to network layer can have gaps (missing datagrams)
  gaps will be filled if app is using TCP
  otherwise, app will see gaps
* Kurose, 2010

## Slide 16: Ethernet Frame Structure
Frame length:
  Min 64 to Max 1518 Bytes (except Preamble, SFD)
Maximum Transmission Unit:
  1500 Bytes (except Preamble, SFD, MAC header, CRC)
Preamble | Start of Frame Delimiter | MAC Destination | MAC Source | Length/Type | Data | CRC
7 Bytes of 10101010 | 1 Byte of 10101011 | 6 | 6 | 2 | 46~1500 | 4

## Slide 17: Ethernet Frame Structure (2)
Preamble:
  7 bytes of 10101010 followed by one byte of 10101011
  To synchronize receiver, sender clock rates
Addresses (6 Bytes)
  Vendor Code (OUI) + Serial Number
  Unique number
Length/Type:
  If > 0x600 => Type (DIX 2.0): indicates higher layer protocol
  If < 0x600 => Length (802.3)
CRC: for error checking

## Slide 18: A-6: Frames and Packets
* Panko, 2010

## Slide 19: Cabling Categories
Cat-1: Traditional phone line, voice
Cat-2: 4 Mbits/sec, voice/data
Cat-3: 10 Mb, voice/data
  Ethernet 10BASE-T, 4 Mb Token-Ring
Cat-4: 16 Mb, voice/data
  Not in use
Cat-5/5e: 100 Mb/1Gb, voice/data
Cat-6: Gigabit Ethernet, voice/data

## Slide 20: A-2: Unshielded Twisted Pair Wiring (UTP) Cord
* Panko, 2010

## Slide 21: Hub
Replicates data it receives onto all ports
Employs star topology
Layer 1 device
Generally refers dummy hub
Does not have traffic monitoring capabilities
  All ports connected to hub can collide with one another (no CSMA/CD)
Switching hub
  Layer 2 device
  Delivers packets to the appropriate port based on the packet's address

## Slide 22: Bridge
Connect two physical segments of a network
Switch: multiport bridge
Bridge: 2 port switch
Not in use => Switching Hub, LAN Switch, Brouter (Bridge + Router)

## Slide 23: Switch
Layer 2 Switch
Each port has a MAC address and forward a data frame to its destined segment/system
Characteristics
  Fast: uses ASIC, not CPU
  Microsegmentation of a network
  Multiport Bridge
  Each port can have a dedicated channel and uses full-duplex
Layer 3 Switch
  Make decisions based on IT address

## Slide 24: Router
Layer 3 device
Connect different logical networks
  Switch, Bridge: connects physical segments on the same logical network
Forward packets based on IP addresses
  Drop packets if the destination is not known
  Need explicit configuration that has routing paths
  Drop MAC-level broadcast traffic

## Slide 25: Virtual LAN (VLAN)
Segment a physical segment into different logical networks
Load balancing, reduced broadcast
Security: Systems on separate VLANs cannot directly talk to each other
Flexibility: use software for reallocation
Type:
  Port-based VLAN (Layer 1)
  MAC address-based VLAN (Layer 2)
  IP address-based VLAN (Layer 3)
  Protocol-based VLAN (Layer 1-3)

## Slide 26: Network Access Control
A user’s computer cannot connect to a network until it meets defined policy standards such as malware protection level, patches, and configuration
A computer should be scanned and checked by a pre-installed software agent prior to the connection
Goals
  Mitigation of zero-day attacks
  Policy enforcement
  Identity and access management
* Wikipedia, 2011

## Slide 27: Network Design
Untrusted zone: Internet
Semi-trusted zone: Web, Mail servers
Trusted zone: DNS for inner network, Database and Application servers
Firewalls:
  Between untrusted zone and semi-trusted zone
  Between semi-trusted zone and trusted zone
  Between entities with different trust levels

## Slide 28: Demilitarized Zone (DMZ)
A computer host or small network inserted as a "neutral zone" between a company's private network and the outside public network
It prevents outside users from getting direct access to a server that has company data
In addition, endpoint security controls, s.a. firewall, antivirus and patch management, should be implemented
* searchsecurity.techtarget.com

## Slide 29: DMZ and Firewalls
* Conklin & White, 2010

## Slide 30: Network Fundamentals Outline
1. Basic Network Concepts
  Network Topologies
  Network Hardware
  Network Design
2. The OSI 7 Layers
3. Internet Protocol
  IPv4
  ARP & RARP
  IPv6
  DNS
4. Transport Protocol
  UDP
  TCP
  ICMP/IGMP

## Slide 31: Network Protocols
Rules, procedures for exchanging data among computer systems
Components of a protocol
  Syntax: data format, encoding
  Semantics: interpretation of patterns, error control
  Synchronization: Sequence control

## Slide 32: OSI reference model
Developed by Internal Standards Organization (ISO)
Deals with connecting open systems – system that are open for communication w/ other systems
Has 7 layers
  Each has a different level of abstraction
  Each performs a well defined function
  Each layer’s function defines internally standardized protocols
  The layer boundaries chosen to minimize the information flow across the interfaces
  The number of layers should be large enough and small enough
* Tanenbaum, 1996

## Slide 33: OSI Layers
Layer | Function | Protocols or Standards
L7: Application | Provides services s.a. email, file transfers, and file servers | HTTP, FTP, DNS, SNMP, MIME
L6: Presentation | Provides encryption, code conversion, and data formatting | MPEG, JPEG, TIFF
L5: Session | Negotiates and establishes a connection w/ another computer | SQL, X-Windows, RPC
L4: Transportation | Supports end-to-end routing across networks | TCP, UDP, SPX
L3: Network | Performs packet routing across networks | IP, ICMP, ARP
L2: Data link | Provides error checking, and transfer of message frames | Ethernet, Token Ring, 802.11
L1: Physical | Interfaces w/ transmission medium and sends data over the network | EIA RS-232, EIA RS-449, IEEE 802
* Cole, 2009

## Slide 34: Functions of OSI Layers

## Slide 35: Data Link, Physical Layer
Physical
  Transmission and reception of the unstructured raw bit stream over a physical medium
Data Link
  Provide connection between the physical parts (e.g., cables) w/ the above layer
    Address Resolution Protocol (ARP)
    Reverse Address Resolution Protocol (RARP)

## Slide 36: Network Layer
Routing
Addressing
Error detection
Node traffic control
  The Internet Protocol (IP)
  Internet control message protocol (ICMP)

## Slide 37: Transport Layer
Accept data from the session layer, break it up, pass these to the network layer, and ensure the correct delivery at the other end
  Transmission Control Protocol (TCP)
  User Datagram Protocol (UDP)
    UDP is preferred over TCP when
      Real time communication
      Repetitive info: the impact of one packet lost is minimal
      Excessive overhead: TCP overhead causes performance issues

## Slide 38: Session Layer
Establishing the connection
Transferring data
Releasing the connection
  Structured Query Language (SQL)
  X-Window System
  Remote Procedure Call (RPC)

## Slide 39: Presentation Layer
Present information to the Application layer
Puts info in a unified format so that computers can communicate
Encryption, decryption, compression, and decompression, translate codes s.a. EBCDIC or ASCII
  Motion Picture Experts Group (MPEG)
  Joint Photographic Experts Group (JPEG)
  Tagged Image File Format (TIFF)

## Slide 40: Application Layer
The interface to the user
Identifies the desired recipient of the communication.
  File Transfer Protocol (FTP)
  Domain Name Service (DNS)
  Simple Mail Transfer Protocol (SMTP)
  Simple Network management Protocol (SMNP)
  Remote login (Rlogin)
  Multiple Internet Mail Extensions (MIME)

## Slide 41: Layered Standards Architectures
* technet.microsoft.com, 2003

## Slide 42: TCP/IP Model Layers
Layer | Function | Protocols or Standards
Application | A process above the Transport Layer Communicates via sockets and ports | SMTP, POP, HTTP, FTP
Host-to-Host or Transport Layer | Performs packet sequencing Supports reliable end-to-end communications Ensures data integrity Provides for error-free delivery | TCP, UDP
Internet Layer | Isolates the upper-layer protocols from the details of the underlying network and manages the connections across the network Uses protocols that provide for logical transmission of packets over a network and controls communication Assigns IP addresses to network nodes | IP, ICMP
Network Access Layer | Mapping IP addresses to MAC addresses and encapsulation of IP datagrams into frames to be transmitted by the network Comm. h/w and s/w, connectors, voltage levels, and cabling | ARP, RARP, EIA RS-232, EIA RS-449, IEEE 802
* Cole, 2009

## Slide 43: TCP/IP Encapsulation
* learn-networking.com, 2011

## Slide 44: Network Fundamentals Outline
1. Basic Network Concepts
  Network Topologies
  Network Hardware
  Network Design
2. The OSI 7 Layers
3. Internet Protocol
  IPv4
  ARP & RARP
  IPv6
  DNS
4. Transport Protocol
  UDP
  TCP
  ICMP/IGMP

## Slide 45: 3. Internet Protocol
Delivers packet via the Internet
TCP, UDP, ICMP uses IP
Has the addressing scheme
Provides best-effort service: no error control, no flow control
Connectionless, unreliable
  Relies on upper layers
IPv4 -> IPv6

## Slide 46: IPv4 Packet Structure
Total Length
(16 bits)
Identification (16 bits)
Header Checksum (16 bits)
Time to Live
(8 bits)
Flags
Protocol (8 bits)
1=ICMP, 6=TCP,
17=TCP
Bit 0
Bit 31
Source IP Address (32 bits)
Fragment Offset (13 bits)
Type of Serv.
(8 bits)
Header
Length
(4 bits)
Version
(4 bits)
Destination IP Address (32 bits)
Options (if any)
Padding
Data Field
0100

## Slide 47: IP Header Key Fields
Version: IP protocol version number
Header Length: header length (bytes)
Type of Service: “type” of data
Length: total datagram length (bytes)
16-bit identifier, Flags, Fragment Offset: For fragmentation/reassembly
time to live: max number remaining hops (decremented at each router)
Protocol: upper layer protocol to deliver payload to
Optional: E.g. timestamp, record route taken, specify list of routers to visit.

## Slide 48: IP Packets Encapsulation into Ethernet Frames
Min IP packet length:
Max IP packet length:
Max MTU of Ethernet:
How many frames are necessary to carry one maximum-sized IP packet?

## Slide 49: IPv4 Addresses
An address consists of the network portion of the address (net-id) and the host portion (host-id)
Displayed as 4 numbers separated by periods
Some addresses are reserved
  The first address in a network (all 0s address of the host portion): the network address
  The last address in a network (all 1s address of the host portion ): the broadcast address
  Directed broadcast: passes by routers

## Slide 50: Subnetting
Consider 10.10.10.101
  IP Address: 10.10.10.101
  Subnet Mask: 255.255.255.0
  Net-id? Host-id?
  How to get the network address?
CIDR (Classless Inter-Domain Routing)
  Uses variable length subnet masks to allocate IP addresses to subnets
  10.10.10.101/16
    => uses 16 bits for net-id

## Slide 51: IPv4 Address Classes
Class A
  The first bit = 0 (=> 1-127)
  N.H.H.H
  255.0.0.0 (/8)
Class B
  The first two bits = 10 (128–191)
  N.N.H.H
  255.255.0.0 (/16)
Class C
  The first three bits = 110 (192-223)
  N.N.N.H
  255.255.255.0 (/24)
* Conklin & White, 2010

## Slide 52: Private Address
Private address
  10.0.0.0 – 10.255.255.255
  172.16.0.0 – 172.31.255.255
  192.168.0.0 – 192.168.255.255
They are not routed
Compensate for the shortage of public IP addresses
Use Network Address Translation (NAT) to map private (nonroutable) IP addresses into public (routable) IP addresses

## Slide 53: NAT vs DHCP
Network Address Translation (NAT)
Dynamic Host Configuration Protocol (DHCP)
How do your home network connect to the Internet?

## Slide 54: MAC Address & IP Address
MAC address (Layer2 - Data Link layer)
  48-bit (6 byte) address, burned into the ROM of the NIC (Network Interface Card)
  Also called the Hardware address, or Ethernet address
  Expressed as six pairs of hexadecimal digits
IP address (Layer 3 - Network layer)
  32-bit (4 byte) software stored address
  Assigned to represent the same NIC as MAC address represents
  Like a shorter nickname for the 48-bit MAC address
* Source: infocellar.com

## Slide 55: Packet Delivery
Packets delivered on a network (e.g., LAN)
  Use the Media Access Control (MAC) address
  Address Resolution Protocol (ARP): IP address -> MAC address
Packet delivery to a remote system
  Use the Internet Protocol (IP) address
  Use the Domain Name System (DNS) protocol to convert IP addresses to hostnames
* Conklin & White, 2010

## Slide 56: ARP & RARP
Address Resolution Protocol (ARP)
  Address resolution protocol that converts logical IP address to physical MAC address (layer 2 protocol)
  Router sends a broadcast to the network: “Who has 10.10.10.101? Tell 10.10.10.102”. The host 10.10.10.101 should reply with its MAC address.
  ARP cache: the new entry is placed in the cache
Reverse Address Resolution Protocol (RARP)
  Obtain IP address from MAC address
  Not in use -> instead use DHCP (Dynamic Host Configuration Protocol)

## Slide 57: Limitations of IPv4
The recent exponential growth of the Internet and the impending exhaustion of the IPv4 address space
The growth of the Internet and the ability of Internet backbone routers to maintain large routing tables
The need for simpler configuration
The requirement for security at the IP level
The need for better support for real-time delivery of data—also called quality of service (QoS)
* technet.microsoft.com, 2011

## Slide 58: IPv6 Features
New header format
Large address space
Efficient and hierarchical addressing and routing infrastructure
Stateless and stateful address configuration
Built-in security
Better support for prioritized delivery
New protocol for neighboring node interaction
Extensibility
* technet.microsoft.com, 2011

## Slide 59: Differences Between IPv4 and IPv6
IPv4 | IPv6
Addresses are 32 bits (4 bytes) in length. | Addresses are 128 bits (16 bytes) in length
IPsec support is optional | IPsec support is required
No QoS handling by routers | Quality of Service (QoS) included in the header
Header includes a checksum | Header does not include a checksum
Header includes options | All optional data is moved to IPv6 extension headers
ARP uses broadcast ARP Request frames to resolve an IPv4 address to a link layer address | ARP Request frames are replaced with multicast Neighbor Solicitation messages
* technet.microsoft.com, 2011

## Slide 60: IPv6 Address
IPv4: supports 232 (4,294,967,296)
IPv6: supports 2128 (340 undecillion) addresses (7 addresses per person)
Example:
  2001:0DB8:0000:2F3B:02AA:00FF:FE28:9C5A
Global Unicast Addresses
* technet.microsoft.com, 2011

## Slide 61: Structure of an IPv6 Packet
Priority: identify priority among datagrams in flow
Flow Label: Used for QoS functionality
Next Header: identify upper layer protocol for data

## Slide 62: Domain Name System
Translates names into IP addresses
The initial solution for name resolution
  Use Hosts.txt used on ARPANET
  Computers on the ARPANET periodically downloaded Hosts.txt from a central location
Domain Name System
  Defines a namespace and a protocol for name resolution and database replication
  Has a hierarchical and logical tree structure
  DNS queries sent over UDP first. The hosts (DNS clients) resort to TCP only if the returned data is truncated
* technet.microsoft.com, 2011

## Slide 63: DNS Domain Names
Types of DNS Domain Names
  Root domain: “” or . (period)
  Top level domain: “com”
  Second level domain: “microsoft.com”
  Subdomain: “mydomain.microsoft.com”
  Host or resource name: “host-a. mydomain.microsoft.com”
Generic top-level domains (as of Sep, 2011)
  aero, asia, biz, cat, com, coop, edu, gov, info, int, jobs, mil, mobi, museum, name, net, org, pro, tel, travel, xxx (total 21)
Country code top-level domains
  ac, ad, ae, af, ag, ai, al, am, an, etc
* technet.microsoft.com, 2011

## Slide 64: DNS Hierarchy
* technet.microsoft.com, 2011

## Slide 65: DNS Query
* technet.microsoft.com, 2011

## Slide 66: DNS in TCP/IP
* technet.microsoft.com, 2011

## Slide 67: DNS Security Threats
Threats
  Footprinting: DNS zone data is obtained by an attacker (info leakage)
  Denial-of-service attack
  Data modification (IP spoofing): use valid IP addresses in IP packets the attacker has created
  Redirection (cache poisoning)
Defenses
  Limit zone transfers to specified IP addresses
  Enable secure cache against pollution
  Place DNS server on a perimeter network
  Add a secondary server on another subnet or network
* technet.microsoft.com, 2011

## Slide 68: Network Fundamentals Outline
1. Basic Network Concepts
  Network Topologies
  Network Hardware
  Network Design
2. The OSI 7 Layers
3. Internet Protocol
  IPv4
  ARP & RARP
  IPv6
  DNS
4. Transport Protocol
  UDP
  TCP
  ICMP/IGMP

## Slide 69: User Datagram Protocol (UDP)
Connectionless service; no session is established between hosts
UDP does not guarantee or acknowledge delivery, or sequence data
Programs that use UDP are responsible for providing any reliability needed to transport data
UDP is fast, has low overhead requirements, and can support point-to-point and point-to-multipoint communication
* technet.microsoft.com, 2011

## Slide 70: Values of UDP
Voice and video traffic - real-time video and audio streaming protocols
Multicasting
DNS queries
  A single UDP request from the client
  A single UDP reply from the server
UDP ports
  A location for sending and receiving UDP messages.
  UDP port numbers: 53 (DNS), 67 and 68 (Bootp), 69 (TFTP), 161 (SNMP), 2049 (NFS)

## Slide 71: UDP Header
0 – 15 | 16 – 31
SRC Port Number | DST Port Number
Length | Checksum
Data (Variable) | 
* technet.microsoft.com, 2011

## Slide 72: Transmission Control Protocol (TCP)
Connection-oriented service; a session is established between hosts
TCP guarantees delivery through the use of acknowledgments and sequenced delivery of data
Programs that use TCP are provided assurance of reliable data transport
TCP is slower, has higher overhead requirements, and only supports point-to-point communication
TCP Ports
  20 (FTP-data), 21 (FTP-control), 23 (Telnet), DNS (53), 80 (HTTP), 110 (POP), HTTPS (443)
* technet.microsoft.com, 2011

## Slide 73: TCP Segment
Source Port Number (16 bits)
Destination Port Number (16 bits)
Acknowledgment Number (32 bits)
Sequence Number (32 bits)
TCP Checksum (16 bits)
Window Size
(16 bits)
Flag Fields
(6 bits)
Reserved
(6 bits)
Header
Length
(4 bits)
Urgent Pointer (16 bits)

## Slide 74: TCP Fields
Sequence number, Acknowledgement number: counting by bytes of data (not segments!)
Flag fields:
  U: URG: urgent data (generally not used)
  A: ACK: ACK # valid
  P: PSH: push data now (generally not used)
  R, S, F: RST, SYN, FIN: connection estab (setup, teardown commands)
Receive window: # bytes receiver willing to accept
Checksum: Internet checksum (as in UDP)

## Slide 75: Three Way Handshake
Step 1 (client): sends SYN segment to the server
  The segment has initial client seq #
Step 2 (server): receives SYN, replies with SYN/ACK segment
  The server allocates buffers
  The server segment has initial server seq. #
Step 3 (client): receives SYN/ACK and replies with ACK segment

## Slide 76: Closing a Connection
Graceful closure
  Step 1 (client): sends FIN segment to server
  Step 2 (server): receives FIN and replies with ACK. Closes connection and sends FIN
  Step 3 (client): receives FIN and replies with ACK
  Step 4 (server): receives ACK. Connection closed
Abrupt closure
  Send RST from either side

## Slide 77: Messages in a TCP Session (1)
PC
Transport Process
Webserver
Transport Process
1. SYN (Open)
2. SYN, ACK (1) (Acknowledgement of 1)
3. ACK (2)
Open
(3)
3-Way Open

## Slide 78: Messages in a TCP Session (2)
PC
Transport Process
Webserver
Transport Process
1. SYN (Open)
2. SYN, ACK (1) (Acknowledgement of 1)
3. ACK (2)
4. Data = HTTP Request
5. ACK (4)
6. Data = HTTP Response
7. ACK (6)
Open
(3)
Carry
HTTP
Req &
Resp
(4)

## Slide 79: Messages in a TCP Session (3)
PC
Transport Process
Webserver
Transport Process
8. Data = HTTP Request (Error)
Carry
HTTP
Req &
Resp
(4)
9. Data = HTTP Request (No ACK so Retransmit)
10. ACK (9)
11. Data = HTTP Response
12. ACK (11)
Error Handling

## Slide 80: Messages in a TCP Session (4)
PC
Transport Process
Webserver
Transport Process
Close
(4)
13. FIN (Close)
14. ACK (13)
15. FIN
16. ACK (15)
Note: An ACK may be combined with the next message if the next message
is sent quickly enough
Normal Four-Way Close

## Slide 81: Messages in a TCP Session (5)
PC
Transport Process
Webserver
Transport Process
Close
(1)
RST
Abrupt Close
Either side can send
A Reset (RST) Segment
At Any Time
Ends the Session Immediately

## Slide 82: Internet Control Message Protocol (ICMP)
A control and information protocol and is used by network devices
  Determine a remote network’s availability, the length of time to reach a remote network, and the best route for packets to take
Provides troubleshooting facilities and error reporting for packets that are undeliverable
Probably the third most commonly used protocol
Network-layer “above” IP
  ICMP messages carried in IP datagrams
* technet.microsoft.com, 2003

## Slide 83: Common ICMP Messages
ICMP Message | Function
Echo Request | Troubleshooting message used to check IP connectivity to a desired host. The ping utility sends ICMP Echo Request messages
Echo Reply | Response to an ICMP Echo Request
Redirect | Sent by a router to inform a sending host of a better route to a destination IP address
Source Quench (elective message) | Sent by a router to inform a sending host that its IP datagrams are being dropped due to congestion at the router. The sending host then lowers its transmission rate.
Destination Unreachable | Sent by a router or the destination host to inform the sending host that the datagram cannot be delivered
* technet.microsoft.com, 2003

## Slide 84: Internet Group Management Protocol (IGMP)
Manages host membership in IP multicast groups (host groups) on a network segment
  An IP multicast group is a set of hosts that listen for IP traffic destined for a specific IP multicast address
IP multicasting
  Host group membership is dynamic, hosts can join and leave the group at any time
  A host group can be of any size
  Members of a host group can span IP routers across multiple networks
  A host can send traffic to an IP multicast address without belonging to the corresponding host group

## Slide 85: Utilities
cmd
  Microsoft-supplied command-line interpreter
ipconfig
  Displays all current TCP/IP network configuration values
traceroute
  Determines the route to a destination
  Windows “tracert” uses ICMP) echo packets to the destination
  UNIX “traceroute” uses UDP packets
netstat
  Viewing ports

## Slide 86: Network Fundamentals Outline
1. Basic Network Concepts
  Network Topologies
  Network Hardware
  Network Design
2. The OSI 7 Layers
3. Internet Protocol
  IPv4
  ARP & RARP
  IPv6
  DNS
4. Transport Protocol
  UDP
  TCP
  ICMP/IGMP
5. Packet Analysis
  IP
  TCP

## Slide 87: Packet Analysis
Uses hexadecimal numbers
  Base is 16
  Notation: “0x”
  11111111 (binary) => 255 (decimal)
    Hex: ???
  Offsets start at 0
  8 bits (a byte) = two hex characters

## Slide 88: Hexadecimal Numbers
23 | 22 | 21 | 20 | Hex
0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 1
0 | 0 | 1 | 0 | 2
0 | 0 | 1 | 1 | 3
0 | 1 | 0 | 0 | 4
0 | 1 | 0 | 1 | 5
0 | 1 | 1 | 0 | 6
0 | 1 | 1 | 1 | 7
23 | 22 | 21 | 20 | Hex
1 | 0 | 0 | 0 | 8
1 | 0 | 0 | 1 | 9
1 | 0 | 1 | 0 | a (10)
1 | 0 | 1 | 1 | b (11)
1 | 1 | 0 | 0 | c (12)
1 | 1 | 0 | 1 | d (13)
1 | 1 | 1 | 0 | e (14)
1 | 1 | 1 | 1 | f (15)

## Slide 89: A Sample Frame: 66 bytes (528 bits)
Ethernet II (DEX Ethernet): 14 bytes
Internet Protocol Version 4: 20 bytes
Transmission Control Protocol: 32 bytes
00 22 5f 58 2b 0d 00 13 46 cc a3 ea 08 00 45 20
00 34 d5 6e 00 00 37 06 8f 34 4a 7d 13 69 c0 a8
00 73 00 50 60 9a 0e 02 d5 0d 7a d1 01 0c 80 12
16 58 79 ef 00 00 02 04 05 96 01 01 04 02 01 03
03 06

## Slide 90: IP Header (1)
45 20 00 34
d5 6e 00 00
37 06 8f 34
4a 7d 13 69
c0 a8 00 73
(1) Version: 4
(2) IHL: 5
(3) Type of Service
(ToS): Priority
0010 00..
.... ..00
(4) Total length:
0x34 (52)
(1)
(2)
(3)
(4)
Notes: * Type of Service: http://www.freesoft.org/CIE/Course/Section3/7.htm

## Slide 91: IP Header (2)
45 20 00 34
d5 6e 00 00
37 06 8f 34
4a 7d 13 69
c0 a8 00 73
(5) IP Identification:
0xd56e (54638)
(6,7) Flags, Fragment offset:
0x0000 = 0000 0000 0000 0000
(5)
(6,7)
Notes: * Type of Service: http://www.freesoft.org/CIE/Course/Section3/7.htm

## Slide 92: IP Header (3)
45 20 00 34
d5 6e 00 00
37 06 8f 34
4a 7d 13 69
c0 a8 00 73
(8) Time to live: 55
(9) Protocol: TCP (6)
(10) Header
checksum: 0x8f34
(11) Source:
74.125.19.105
(12) Destination:
192.168.0.115
(8)
(9)
(10)
(11)
(12)
Notes: * Type of Service: http://www.freesoft.org/CIE/Course/Section3/7.htm

## Slide 93: TCP Header (1)
00 50 60 9a
0e 02 d5 0d
7a d1 01 0c
80 12 16 58
79 ef 00 00
02 04 05 96
01 01 04 02
01 03 03 06
(1) Source port:
http (80)
(2) Destination port:
24730
(3) Sequence number:
235066637
(4) Acknowledgement
number:
2060517644
(1)
(2)
(3)
(4)

## Slide 94: TCP Header (2)
00 50 60 9a
0e 02 d5 0d
7a d1 01 0c
80 12 16 58
79 ef 00 00
02 04 05 96
01 01 04 02
01 03 03 06
(5) Header length,
Reserved, Flags:
1000 0000 0001 0010
(8=>32, SYN, ACK)
(6) Window size value:
5720
(7) Checksum: 0x79ef
(8) Urgent pointer: 0
(not set)
(5)
(6)
(7)
(8)

## Slide 95: TCP Header (3)
00 50 60 9a
0e 02 d5 0d
7a d1 01 0c
80 12 16 58
79 ef 00 00
02 04 05 96
01 01 04 02
01 03 03 06
(9) Options (12 bytes)
Maximum segment size
(0x0204): 1430 bytes
(0x0596)
(10) Others
(10)
(9)

## Slide 96: Options and Payload Length
Length of packet payload (data) = IP total length – (IP header length + TCP header length)
TCP Options length = TCP header length – Minimum TCP header length (20 bytes)